## Slide 1: The Elusive Internet Flattening: 10 Years of IXP Growth
T. Böttger1, G. Antichi1, E.L. Fernandes1, R. Lallo23, M. Bruyere4, S. Uhlig1, I. Castro1
1QMUL 2 Roma Tre University 3Consortium GARR 4University of Tokyo

## Slide 2: Spoiler
IXP evolution:
  Large growth: # IXPS and members tripled in 2008-2016
  Reachability stagnation: % IPv4 addresses reachable through IXPS has stabilised around 80%
Macroscopic impact?
  Little path-shortening: not one-hop away
  Hierarchical flattening: less transit dependence

## Slide 3
NAP
Hierarchical early Internet
Local access provider
Regional access provider
Tier 1 access provider
Tier 1 access provider
Regional access provider
Local access provider
The early Internet

## Slide 4
Local access provider
IXP
Local access provider
Very few hops, LESS HOPS than ever, we will make no hops at all!!! Trust me!!! #Internetisflat #lesshops
There is LESS TRANSIT DEPENDENCE, in fact the least transit dependence ever!!! #Internetisflat #lesstransit

## Slide 5
IXPs matter for individual ASes
Macroscopic impact???
Internet flattening

## Slide 6: Flattening: Shorter paths?
Hierarchical-early Internet
Flattened-modern Internet
1
2
3
4
5
6
1
2
Many hops
Very few hops, LESS HOPS than ever, we will make no hops at all!!! Trust me!!! #Internetisflat #lesshops

## Slide 7: Flattening: less transit providers?
Hierarchical-early Internet
Flattened-modern Internet
1
2
3
4
Large transit dependence
There is LESS TRANSIT DEPENDENCE, in fact the least transit dependence ever!!! #Internetisflat #lesstransit

## Slide 8: Are there that many IXPs to “flatten” Internet paths??
Historical growth of IXPs:
  Number
  Size
  Reachability

## Slide 9: Data
  IXPs and IXP membership data:
    PeeringDB 2010-2016: CAIDA (https://www.caida.org/data/peeringdb/)
    PeeringDB 2008-2009: “Wayback Machine” (http://archive.org/web/)
  AS-relationships (and T1s):
    2006-2016: CAIDA (http://www.caida.org/data/as-relationships/)

## Slide 10: Large IXP growth over time
In number of IXPs
Rise of new regions
Big stay big

## Slide 11: Large IXP growth over time
In number of IXPs
In number of ASes/members
Rise of new regions
Big stay big
Europe tops growth

## Slide 12
What about reachability?

## Slide 13: ~80% of announced IP’s are reachable via IXPs
100% IPs =
IPs reachable through T1s
(approx. 99% of the IP space)
IPv4 reachability =
IPs that an AS could reach by collocating at an IXP and peering with all its members (T1s excluded)

## Slide 14: ~80% of announced IP’s are reachable via IXPs
few IXPs are enough (for reachability )
Stagnation around 80%

## Slide 15: Large growth of potential peerings at IXPs
Potential peering if 2 ASes are:
  peering (CAIDA)
  Colocated (PeeringDB)

## Slide 16: Large growth of potential peerings at IXPs
Most peering growth is (potentially) IXP-enabled

## Slide 17: How & how much do IXPs matter?
Historical impact of IXPs on Internet paths:
how much have Internet paths “flattened”?
  Reduction of path lengths?
  Reduced transit dependence?

## Slide 18: Data & Methodology
Traceroute data (monthly snapshots)
  iPlane (2006 -2016): from PlanetLab nodes, 2.3 billion traceroutes
  CAIDA Ark (2007-present): from Ark monitors, 4.4 billion
Sanitization of traceroutes (358M Ark, 1.1 billion iPlane)
  destination IP required
  ≥ 1 unresolved IP-hop
  ≥ 1 IXP
Identification of IXPs:
  G. Nomikos & X. Dimitropoulos. “traIXroute: Detecting IXPs in traceroute paths”. PAM 2016

## Slide 19: Path length stability
Path-length is stable out of IXPs
IXPs enjoy a small path-length reduction
IXPs have slightly shorter path lengths

## Slide 20: Some path-shortening for very large networks
15 “Very large large networks”: T Boetger et al., “Looking for Hypergiants in PeeringDB”, ACM CCR 2018

## Slide 21: How meaningful are path-lengths?
Emergence of remote peering:
IXP
AS

## Slide 22: How meaningful are path-lengths?
Emergence of remote peering:
AS
IXP
Remote peering provider

## Slide 23: How meaningful are path-lengths?
Emergence of remote peering:
  Since (at least) 2014 most IXPs have remote peers (Castro et al, CoNEXT 2015)
  On going trend (Nomikos et al, IMC 2018)
CDN redirecting (e.g., Netflix, Castro et al. 2018)
Path-length does not (necessarily) correlate with performance
Impossible to know the traffic volumes corresponding to each route
No vantage point in the Internet has full visibility

## Slide 24: How & how much do IXPs matter?
Historical impact of IXPs on Internet paths:
how much have Internet paths “flattened”?
  Reduction of path lengths?
  Reduced transit dependence?

## Slide 25: Hierarchical flattening: less T1s
Decreasing T1s over time
Less T1s in IXP paths
Notes: “Very large Networks” or hypergiants:
Apple, Amazon, Facebook, Google, Akamai, Yahoo, Netflix, Hurricane Electric, Twitter, Twitch, Cloudflare, Microsoft, Limelight, Verizon (as defined in T. Böttger et al., “Looking for Hypergiants in PeeringDB”. CCR 2018)

## Slide 26: Hierarchical flattening: less transit links
From 2011/2012:
  Decreasing % of transit links at IXPs
  Less transit links in IXP paths
CDNs?
Notes: Calder et al (IMC 2013), Google rapid geo-expansion from 2013
Netflix CDN announced in 2012

## Slide 27: A small number of ASes still play a central role
Divergence in customer cone sizes over time
Divergence vanishes for less central networks
Avg. customer cone size (thousands of ASes)
Ranked in terms of traces traversing an AS
Traces separated depending on whether they traverse and IXP or not
Most central ASes are large & NOW avoid IXPs
Least central ASes are small & “like” IXPs
AS size in terms of reachability/customer cone

## Slide 28: Next things to look at
More data/data bias
CDN emergence
Specific impact of IXP emergence on reduced transit dependence:
  Local benefit of creating an IXP (and its growth)
  Local benefit of the creation of abroad IXPs
Model/predict the emergence/growth of IXPs
Current draft: https://arxiv.org/abs/1810.10963

## Slide 29
Questions?
Thoughts?
…
i.castro@qmul.ac.uk

## Slide 30: More traceroutes traverse IXPs
About the double